## Slide 1: Graph Scattering Convolutional Network
Damian Owerko, Fernando Gama, Alejandro Ribeiro

## Slide 2: Motivation
Convolutional neural networks have demonstrated outstanding image processing performance
Modern signals have an irregular structure (unlike images)  graph signals
  Sensor networks, weather measurements
Extend CNNs to operate on graph signals
  Generalize the convolution operation
Determine power grid brownout using weather measurements
Yan Xu, PhD, Scientist at PROS Follow. "Convolutional neural network." LinkedIn SlideShare. May 20, 2017. Accessed October 22, 2017.
Notes: CNNs
Feature extraction – convolution by set of kernels followed by nonlinearity (pool)
  Levarage knowledge from CNNs on graph signals
Explain why graph signals are useful for weather data
  Geography between stations

## Slide 3: Scattering convolutional network
There are many CNN architectures  we choose the SCN
  Filters pre-specified = no training
    Wavelet filters between layers
  Tune the degree of translation invariance
  State of the art results on MNIST
J. Bruna and S. Mallat, "Invariant Scattering Convolution Networks," in IEEE Transactions on Pattern Analysis and Machine Intelligence, vol. 35, no. 8, pp. 1872-1886, Aug. 2013.
Notes: Move between layers using a band pass filter and extract outputs from each layer using a low-pass filter
Use all outputs for classification (a vector per node)

## Slide 4: Filters can be defined on a graph
Use frequency response of wavelet filter
  is the frequency basis of the underlying graph support
  h is the frequency response  H(h) is the graph filter

## Slide 5: Building the graph support
Graph support that relates the data values
  Weather measurements
  Nodes in the graph are weather stations
Compute distances between stations
  Nearby stations have similar measurements
  Apply gaussian kernel to great-circle distance
Use 25 nodes (stations)

## Slide 6: Preliminary results and future work
Using Earth Networks NYC weather data and EIA reliability data for NY between 2011-2013
Used two Earth Networks dataset fields
  1. temperature – 84.2% accuracy
  2. sea-level pressure – 94.56% accuracy
Much better performance with pressure data
  Likely a better storm predictor
  Optimally combine different weather measurements
  Try other graph CNN architectures

## Slide 7: We extend the SCN to graph signals
SCN
graph SCN